Passive 2-way Line Array with 100 Watt power. Especially suitable for the sound transmission in acoustically difficult rooms.

K4-100F speaker system consisting of:

Passive 2-way Line Array in very stable, resonance-free aluminum housing, assembled with 10 x 3.5“ broadband chassis [LF/MF] and 2 neodymium, highly efficient cylindrical wave tweeter driver in [HF] frequency range. The system has been developed for music- and speech transmission in acoustically difficult room conditions with long reverberation time and demanding room architecture.

The aluminum housing is equipped with a high-grade sound-permeable front grille made of powder-coated aluminum grille and a moisture- and dust-repellent acoustic foam. Surface RAL 9016. The speaker system has sound pressure SPL (1W/1m)@98[db] and a very precise directivity of H-120 degrees x V-20 degrees, the range with SPL/92dB (PINK NOISE) is 18 meter. The speaker system is equipped with an integrated 100 Watt 100V audio transformer and adaption selector switch for nominal power@:1/1,1/2,1/4.

Threaded holes M6 in floor, upper side for entry of mounting brackets are integrated. Simulation files EASE are available.

Deliver, mount, connect

Specifications:

Frequency response: ............. 110 Hz - 18.000 Hz@-3dB

Nominal power@1/1: .................................  100 Watt sine

Nominal power@1/2: ...................................  50 Watt sine

Nominal power@1/4: ...................................  25 Watt sine

Impedance@1/1: ...............................................  100 Ohm

Impedance@1/2: ...............................................  200 Ohm

Impedance@1/4: ...............................................  400 Ohm

Assembly:….....10 x 3.5“ [LF/MF], 2 x 1“ [HF] Neodymium

Audio input: ….........................................................  100V

Reichweite@SPL92dB [PINK NOISE]: .............. 18 meter

Reichweite@SPL95dB [PINK NOISE]: .............  15 meter

Passive switch [LF/HF]: …....………….……… 12db@Oct.

Separation frequency: …....………………….....… 4.5 kHz

Color: ..........................................................      RAL 9016

Dimensions: ................ 1200 (H) x 95 (W) x 113 (D) [mm]

Weight:  ….............................................................. 13.5 kg

Brand: Phoenix Professional Audio GmbH

Type: K4-100F