Passive monitoring line array with 10 Watt power. Especially suitable as controlling system for sound transmission i.e. for monitoring the altar area.

Passive monitoring line array in very stable, resonance-free aluminum housing, assembled with 1 x 3.5“ broadband chassis [LF/MF]. The system has been developed for music- and speech transmission in acoustically difficult space conditions with long reverberation time and demanding room architecture.

The aluminum housing is equipped with a highly sound-permeable front grille made of powder-coated aluminum grille and a moisture- and dust-repellent acoustic foam. Surface RAL 9016. The speaker system has sound pressure SPL(1W/1m)@87[db] and a very precise directivity of H-90 degrees x V-90 degrees, the range at SPL/92dB (PINK NOISE) is 5 meter. The speaker system is equipped with an integrated 10 Watt 100V audio transformer and adaption selector switch for nominal power@: 1/1,1/2,1/4.

Threaded holes M6 in floor, upper side are integrated for entry of mounting brackets. Simulation files EASE are available.

Deliver, mount, connect

Specifications:

Frequency response: ..........    135 Hz - 18.000 Hz@-3dB

Nominal power@1/1: ...................................  10 Watt sine

Nominal power@1/2: ...................................  5 Watt sine

Nominal power@1/4: ..................................  2.5 Watt sine

Impedance@1/1: ...............................................  1 kOhm

Impedance@1/2: ...............................................  2 kOhm

Impedance@1/4: ................................................ 4 kOhm

Assembly: ….......................................   1 x 3.5“ [LF/MF]

Audio input: ….........................................................  100V

Range@SPL92dB[PINK NOISE]: ........................  5 meter

Range@SPL95dB[PINK NOISE]: ........................  3 meter

Color: ..........................................................      RAL 9016

Dimensions: .................. 145 (H) x 95 (W) x 113 (D) [mm]

Weight:  …................................................................ 0.7 kg

Brand: Phoenix Professional Audio GmbH

Type: K4-10F