Passive monitoring line array with 20 Watt power with volume control. Especially suitable as controlling system for sound transmission i.e. for monitoring the altar area.

Passive monitoring line array in very stable, resonance-free aluminum housing, assembled with 2 x 3.5“ broadband chassis [LF/MF]. The system has been developed for music- and speech transmission in acoustically difficult space conditions with long reverberation time and demanding room architecture.

The aluminum housing is equipped with a highly sound-permeable front grille made of powder-coated aluminum grille and a moisture- and dust-repellent acoustic foam. Surface RAL 9016. The speaker system has sound pressure SPL(1W/1m)@90[db] and a very precise directivity of H-90 degrees x V-60 degrees, the range at SPL/92dB (PINK NOISE) is 5 meter. The speaker system is equipped with an integrated 20 Watt 100V audio transformer and adaption selector switch for nominal power@: 1/1,1/2,1/4.

Threaded holes M6 in floor, upper side are integrated for entry of mounting brackets. Simulation files EASE are available.

Deliver, mount, connect

Specifications:

Frequency response: ..........    135 Hz - 18.000 Hz@-3dB

Nominal power@1/1: ...................................  20 Watt sine

Nominal power@1/2: ...................................  10 Watt sine

Nominal power@1/4: ...................................  5 Watt sine

Impedance@1/1: ...............................................  500 Ohm

Impedance@1/2: ...............................................  1 kOhm

Impedance@1/4: ..............................................  2 kOhm

Assembly: ….......................................   2 x 3.5“ [LF/MF]

Audio input: ….........................................................  100V

Range@SPL92dB[PINK NOISE]: ........................  5 meter

Range@SPL95dB[PINK NOISE]: ........................  3 meter

Color: ..........................................................      RAL 9016

Dimensions: .................. 269 (H) x 95 (W) x 113 (D) [mm]

Weight:  …................................................................ 1.0 kg

Brand: Phoenix Professional Audio GmbH

Type: K4-20REG-F