Passive 2-way Line Array with 40 Watt power. Especially suitable for the sound transmission in acoustically difficult rooms.

K4-40F speaker system consisting of:

Passive 2-way Line Array in very stable, resonance-free aluminum housing, assembled with 4 x 3.5“ broadband chassis [LF/MF] and a neodymium, highly efficient cylindrical wave tweeter driver in [HF] frequency range. The system has been developed for music- and voice transmission in acoustically difficult room conditions with long reverberation time and demanding room architecture.

The aluminum housing is equipped with a high-grade sound-permeable front grille made of powder-coated aluminum grille and a moisture- and dust-repellent acoustic foam. Surface RAL 9016. The speaker system has sound pressure SPL(1W/1m)@92[db] and a very precise directivity of H-120 degrees x V-35 degrees, the range at SPL/92dB (PINK NOISE) is 9 meter. The speaker system is equipped with an integrated 40 Watt 100V audio transformer and adaption selector switch for nominal power@: 1/1,1/2,1/4.

Threaded holes M6 in floor and upper side for entry of mounting brackets are integrated. Simulation data EASE are available.

Deliver, mount, connect

Specifications:

Frequency response: ............ 130 Hz - 18.000 Hz@-3dB

Nominal power@1/1: ...................................  40 Watt sine

Nominal power@1/2: ...................................  20 Watt sine

Nominal power@1/4: ...................................  10 Watt sine

Impedance@1/1: ...............................................  250 Ohm

Impedance@1/2: ...............................................  500 Ohm

Impedance@1/4: .................................................  1 kOhm

Assembly: …..... 4 x 3.5“ [LF/MF], 1 x 1“ [HF] Neodymium

Audio input: ….........................................................  100V

Range@SPL92dB [PINK NOISE]: .......................  9 meter

Range@SPL95dB [PINK NOISE]:........................  6 meter

Passive switch [LF/HF]: …....……..………..….12db@Oct.

Separation frequency:…...………………………… 4.5kHz Color:............................................................... RAL 9016

Dimensions: ................... 550 (H) x 95 (W) x 113 (D) [mm]

Weight:  …................................................................ 4.5 kg

Brand: Phoenix Professional Audio GmbH

Type: K4-40F